EBH300(A)  Rock Tunnel Boring Machine

Applications: for the tunneling of rock and semi-rock lanes when the hardness

≤13, also used in the tunneling of highway, railway, and water conservancy

projects. Features:

1.	Computer controlled, wireless remote-controlled, intelligent forming cutting and constant power cutting.

2.	125 tons weight to guarantee the stability and power during cutting.

3.	Advanced centralized lubricating system to guarantee the reliability of every parts

4.	high-efficient separate motor for loading and transporting, more suitable for rock lane boring.

5.	new design of apron, the first class of cutting pick and pick base to guarantee the rock cutting capacity.

# Text boxes

EBH300(A) Rock Tunnel Boring Machine

| Type | EBH300 (A) |
| --- | --- |
| weight（t） | 125 |
| Overall Dimension (L×W×H) (mm) | 12280×3200×2450 |
| Power（kW） | 635 |
| Power Pack（kW） | 150 |
| Cutting Power (kW) | 300 |
| Cutter Speed (rpm) | 20 |
| Telescopic Length (mm) | 650 |
| Width of apron (mm) | 3570 |
| Max. Cutting Height （mm） | 5800 |
| Max. Cutting Width (mm） | 8800 |
| Rock Hardness (MPa) | ≤ 130 |
| Traveling Speed (m/min) | 0~8 |
| Width of Track Shoes (mm) | 720 |
| Ground Pressure Ration (MPa) | 0.22 |
| Load Type | Separate spider |
| Voltage（V） | 1140 |
| Applied Tunnel Gradient | ±18° |